## Slide 1: ECE 485/585 MICROPROCESSOR SYSTEM DESIGN
FALL 2022 – FINAL PROJECT
TITLE – SIMULATION OF LAST LEVEL CACHE(LLC)

## Slide 2: Figure 1: Block Diagram

## Slide 3: Last Level Cache(LLC) Specifications:
Total Capacity : 16 MB
8 - way set associative cache
Line Size : 64 Bytes
Employs write allocate policy
Cache Coherence Protocol – MESI
Replacement Policy – Pseudo LRU

## Slide 4: Address Decoding:
TAG (11 bits) | INDEX (15 bits) | BYTE OFFSET (6 bits)
Address bits (total) = 32 bit

## Slide 5: TRACE FILE FORMAT n address, where n is:
0 - Read request from L1 Data Cache
1 - Write request from L1 Data Cache
2 - Read request from L1 instruction Cache
3 - Snooped invalidate command
4 - Snooped read request
5 - Snooped write request
6 - Snooped read with intent to modify request
8 - Clear the cache and reset all state
9 - Print contents and state of each valid cache line(doesn’t end simulation)
**n=8 , n=9 Project expects address to be 00000000.

## Slide 6: Design decisions for LLC:
Write from L1 will be considered as processor write.
L1 is not part of snoop network, So no MESI in L1.
Data is not used in any of the trace file.
Byte offset need not be stored in the array as we are always dealing with lines.
C in MESI FSM is modelled in RTL and not in Validation under the module “Cache_get_snoop_function”.
Flush in MESI FSM is considered as Bus Operation Write.
When HITM is present, Processor is not modelling the delay where Flush will happen and after which CPU2 will read the bus.

## Slide 7: Design decisions for LLC:
Not modelling Outgoing HIT, HITM or NOHIT.
Always assumes that L1 has the data to be evicted and L2 will send the EVICTLINE command, regardless.
Snoop operation on a line will make the line recently used.
Assuming a random clock delay of 100 cycles between successive operations.
Snoop on a line is also considered for hit and miss(counters).
Upon (n==8) design is clearing the hit and miss counters as well.